Merging of tester and test item
The following sub-chapters will deal with the problems occurred during the consolidation. From the beginning of this thesis it was expected that this part of development will cause problems which need to be fine-tuned and/or solved. Due to the circumstance of the used alternative hardware (see chapter XYZ INTRODUCTION on page ZYX), several more problems and workarounds occur during the consolidation. As far as possible it must be taken into account that the workarounds are functional on the alternative devices.
  1. Analysis and solution of accrued problems
    1. Communication
The communication between both devices is based on an already finished and proved communication protocol. It stands for one of the major parts of the development, because the complete environment is based on this.
Originally it was expected that the implementation of this protocol will only cause minor problems concerning the task stack size and minimal timing difficulties. During the consolidation it turned out that the communication protocol is based on a half-duplex communication interface. This means that a member of the communication can either read or write but is not able to do both coevally. In general, a RS 485 interface is built in full-duplex with five wires, of which two represent plus and minus either for transmit and receive and the fifth line represents the interface GND signal. The mode-reducing is effected by an special component. It is built to normally just read from the interface and only to be enabled to write by setting the ENABLE signal. The special component with its internal connection is shown in figure 1.
In the considerations it was expected that the test item also contains two half-duplex RS 485 interfaces. During the first communication attempt this mistake was found because the protocol was not able to establish a connection. During the debugging phase it turned out that the testee was either able to send or to read. But the normal protocol functionality includes confirmation as well as pure data packages which comes out to the fact that a normal operation is only possible with a two-way communication. Even without confirmation data transfer in both directions is necessary because the test item needs to send test results back to the test device.
Figure 1: RS 485 full-to-half-duplex mode changer
There are five possible solution statements for the communication problems, which more or less interfere with the hard- and/or software of both devices. Firstly it is possible to change the testers RS 485 interface to full-duplex mode as well. On first sight this seems to be the easiest solution. Beside of the complex patchwork on the test device PCB this possibility also enforces changes to the interface driver software as well. Another reason against this option is the fact that the PCB changes are not allowed to be done on the alternative hardware. Because of that, no further development would be possible as long as the tester device becomes available, which costs a lot of time. Thus this possibility is no option. The second possible solution would be the modification of the full-duplex interface on the test item. In fact this option requires at first the patching and afterwards the de-patching of the RS 485 connection and also changes to the Linux kernel system, which makes this solution even more unhandy than the first one. A third solution is an additional piece of hardware which is connected to the RS 485 interface of the test item and reduces the transfer to half-duplex mode. Although this option does not require any patchwork it costs develop- as well as assemble time and enforces changes to the Linux kernel as well as the second option. As a forth option it is possible to change the communication interface. Basically a RS 485 interface is driven by an UART which means that any other UART connection may be used instead of the RS 485 connection. The test item contains one more interface driven by an UART, which is the RS 232 serial connection. Unfortunately this connection is already used by the operating system as standard input and output for commands and messages. With the use of this connection for the communication it will not be possible any more to interact manually with the Linux operating system. Also it would not be possible to print out messages to a terminal.
Lastly is possible to modify the protocol software on the test device to use both available RS 485 interfaces to create a full-duplex transfer. The advantage of this method is that no patchwork is required and that this solution is runnable both on the original test device as well as on its alternatives. Furthermore the required software changes are minimal because in the end only the central read and write calls must be modified to work with the right interface. Fortunately this both calls are each only once used in the protocol and are not able to collide. In order to be able to modify the interface number used to write and read, the protocol initialisation is extended with arguments to set these configuration manually.
    1. test sequences

  1. Adjustment of applications
Several parts of the software require a fine-adjustment or special additions in order to create a fully applicable test environment. This mostly concerns the communication between both devices as well as necessary wait-states on certain code locations.
    1. Remote access
The communication protocol is a circular system. This means that a call from outside is usually not executed immediately but on the next cycle. This certainty causes a natural delay which must be taken into account if a two-way data transfer is requested. The easiest method to handle this problem is a blocked programming based on semaphores.
Table 1: Flow example with and without semaphore blocking
Master	Slave
Software activity
Data gets written / Call result function to note that the writing is finished / Driver reads result handled from result function and quits afterwards / Call function on test item to write data to an output / Flow 1 / Flow 2 / Wait for semaphore release or time out / Result function is called and semaphore released	Function to write data to an output is called

Table 1 shows the main difference between a blocked and a non-blocked two-way transfer. The non-blocked method (Flow 1) automatically reads the result created by the result function right after the remote call. The remote device is not able to execute the requested command and to call the result function within this short time. If the result function was already used before, the previous result is still active and will be used instead of the new requested one. In worst case the result is not initialised and contains meaningless information. This circumstance leads to a undesired software behaviour which is hard to debug. The blocked method (Flow 2) is extended with an semaphore which is requested right after the remote function call. The semaphore is already taken and will be released as last statement of the result function. This approach assures that the remote function was executed and finished and the result was generated. A further advantage of this method is the prevention of deadly time-outs. The request for a semaphore is able to be bound to a maximum time. In case of a fault the semaphore will not be released within the specified time and the request returns an error. The detailed semaphore approach is shown in figure 2. The mentioned three seconds in this figure are a sample value. During the merge of the devices it will be necessary to improve such values. These timings do not have to be very hazardous because the test environment has no claims to act as a high performance system. In general it is expectable that the communication is workable. The time-out represents the worst case and should only be entered if the collapse of the regular communication is definitely assured. Every time-out will automatically cause a negative test result. It must be taken into account that this in turn enforces a manual check-up which takes a lot more time then a generous calculated time-out.
Figure 2: Flow chart of the block method
    1. General wait-states
The FreeRTOS provides a function to hold a task for a certain time (see chapter XYZ FREERTOS on page ZYX). In several parts of the software, a so-called wait-state increases the reliability and functionality.
One of the most important wait-states is implemented to the command-line interpreter. The menu structure is designed that way to wait for incoming data the whole time. Because of that, the read-statement is written into a loop which is only quit if a command has been inserted. Without a wait-state within here, the operating system would spend all calculation time of the processor only for this loop. This in turn implies that no calculation time is left for the circular communication protocol or other tasks running in the background. Code 1 shows the input loop mechanism. The wait-state holds the loop for ten microseconds, which frees enough calculation time for all other tasks. In turn there is no risk to miss an incoming character because no human is able to type with that speed.

UINT8 buffer; /* Contains the momentary received character */
BOOLEAN receive; /* Indicates whether a character is available */

do /* Do-while loop for String input */
    {
    if ((receive = serGet(MenuPort, &buffer) == TRUE))
        {
        /* Key detection algorithms */
        }
    vTaskDelay (10); /* Share Calculation Time to FreeRTOS */
    } while (buffer != 13); /* Read input until ENTER-Key */
Code 1: Menu input loop with implemented wait-state
Apart from the command-line interpreter, wait-states are usually used to make assure that a previous command was executed. This is for instance used in the analogue connectivity sequences; if an in- or output is switched between voltage and current it is necessary to wait a certain time until the mode is changed. It is not possible to get any feedback to make sure that the mode-change is finished. The same holds for some more cases in which it is not possible to clamp the status of a certain command. Usually a wait-state represents a less complex method to assure the completion of a previous function. The hold-times must be adjusted during the merge. In general it is possible to use more generous values, which in turn may be unhandy if the corresponding code sequence is used more often.

Development of the test environment control software
The test environment developed within this paper will be used by several employees. Because of this, it is one ambition of this thesis to create an as far as possible easy-to-use application. Although the command-line interpreter allows interaction to control the environment, it needs a certain time get used to the usage. In order to simplify the control, a window application will be created.
The development of a window application for Windows operating system is possible in several programming languages and environments. Because of company-internal experience the application will be developed in C# within the Visual Studio software.
Basically the C# code is separable to two different purposes of which the first controls the window behaviour and the second one the conventional, executable application. C# is a object-orientated language and is so unlike the software developed in ANSI C able to remain within the application without the need of an endless loop. Furthermore C# is able to control multiple tasks and instances which allows among others the run of an own time-out task running parallel to the common application.
The window application uses a COM port of the PC on which it is executed to communicate with the tester device. Basically the control mechanism consists of several function calls, which can also directly be handled to the command line. For the other direction a interpreter must be created which is able to filter keywords sent from the tester device, for instance test results or error messages.
The application allows an dynamic automation in which test sequences can be en- or disabled. Also all tests can be called individually. Furthermore the application is able to show and calculate test statistics and save the test results in log files.
Due to the circumstance mentioned in the Introduction (see page XYZ), the control application can not be completed within this paper. In order to create and show a general functionality, the digital, analogue and relay connectivity tests are controllable. The application surface is displayed in figure 3. As shown, each available test is either executable individually or within a series with all activated tests. The upper right area contains detailed test-flow options. The lower right side shows the test statistics.

Figure 3: control application surface