Software development
The complete software of this thesis is written in ANSI C with only a few exceptions on some register commands and interrupt handling that can only be done in Assembler. The software is basically split into the two different chapters 1.1. Tester and 1.2. Test item, which are both divided to several sub-projects.
  1. Tester
The software for the tester device is split into several sub-projects, which is on the one hand caused by a better abridgement but on the other hand makes the individual software parts much easier portable to other projects based on the same processor architecture. Some parts like the file-system library are totally platform-independent.
The following chapters explain and deal with the individual software parts. The annotations are kept to the more general functionality of the code and will not be too detailed. Only basic approach used in the whole project (for instance register manipulation) or very special program sequences will be clarified with example code lines or the corresponding, special code section. Also, special approach of code-style is shown with short examples in the chapter, where the example belongs to.
As far as possible, already written code or software parts, which are only assumed to this thesis, will be marked as so. Every code file in the addendum got an file header, in which the initials of the author or authors and the date of the file creation is mentioned. Foreign sources such as open source projects contain own file headers with their licence agreement, which regulates the private and commercial use of this code.
The most parts of the software mentioned and explained in the following chapters were created and tested on the target hardware. Nevertheless, the complete software is based on the considerations from chapter CONSIDERATIONS on page XYZ. Occurring problems with this software during the development and testing/debugging of the complete test environment with the testee will be mentioned, explained and (if possible) solved in chapter MERGE on page ZYX.
    1. Type definitions and code style
The company supporting this thesis uses an own coding standard as well as own data type definitions. This is mainly caused by the several different platforms and architectures used with the different projects of the company. The own data types are to keep a maximised level of portability and readability of the code. The main problem of data types in C-code is, that some of them differ in size, depending on the processor architecture on which they are applied. For instance, the common type int differs between sizes of two and eight bytes. Also, common data types can be used signed or unsigned, which is also important on embedded systems. The following code fragment 1 shows the type definition used on the 32-bit ARM processor.

#define UINT8 unsigned char /* Definition of type unsigned 8 Bit */
#define UINT16 unsigned short /* Definition of type unsigned 16 Bit */
#define UINT32 unsigned int /* Definition of type unsigned 32 Bit */

#define pUINT8 unsigned char * /* Definition of pointer to type unsigned 8 Bit */
#define pUINT16 unsigned short * /* Definition of pointer to type unsigned 16 Bit */
#define pUINT32 unsigned int * /* Definition of pointer to type unsigned 32 Bit */

#define INT8 char /* Definition of type signed 8 Bit */
#define INT16 short /* Definition of type signed 16 Bit */
#define INT32 int /* Definition of type signed 32 Bit */

#define pINT8 char * /* Definition of pointer to type signed 8 Bit */
#define pINT16 short * /* Definition of pointer to type signed 16 Bit */
#define pINT32 int * /* Definition of pointer to type signed 32 Bit */

#ifndef NULL /* If NULL was defined up to now */
#define NULL (0) /* Definition of NULL */
#endif

typedef enum /* Define own enumeration type BOOLEAN */
{
  FALSE = NULL, /* Set FALSE to NULL */
  TRUE /* Set TRUE to 'NOT FALSE' */
} BOOLEAN;

typedef enum /* Define own enumeration type RESULT */
{
  ERROR = 0, /* Set ERROR as a Result member */
  OK /* Set Result OK to 'NOT ERROR' */
} RESULT;
Code 1: Own data type definitions
The coding standard describes the way code is to be formatted within the code files. This is on the one hand to increase the serviceability of the software as well as the readability, but on the other hand decreases the dependency to the software author. For instance, the coding standard regulates in which way comments are to be written within the codefiles. Code 1 shows a more simple example of these regulations, where all comments start and end at the same column.
    1. Hardware configuration
The hardware configuration of the processor is split into four different parts and several different files of the project. The most elementary part is the linker script, which is used by the compiler to manage the memory parts of the processor. The used LPC 2388 processor contain several different memory sections like the FLASH to store the software code and a general RAM[1] section on which variables are created and commands are executed. Moreover, the ethernet and the USB interfaces contain own, small RAM sections to store the corresponding stacks. These Sections are all mentioned in the linker script.
[1] RAM:	Random access memory
The second part is the basic processor configuration, which mainly consist of the different clock settings. Although the processor component is attached to only two different crystals, the internal devices and interfaces need several different clock cycles. This is done by internal clock prescalers, which are to be configurated, set and enabled as one of the first steps done with the processor boot up. In fact, the complete clock management depends on the external 12 MHz oscillator. The second crystal of 32,768 kHz is exclusively used by the internal realtime clock.
Where the first two parts of the processor set up are more general settings which can be used on almost every project based on the LPC 23xx family and are set before any application can be called, the other two steps depend much more on the application(s) executed on the processor. The next step is the enabling and configuration of used internal devices like the interrupt vectors, the memory acceleration module or the watchdog module. The last hardware set up part is the pin configuration. These settings depend only on the application and the attached periphery and are set just in the application using these pins.
Any hardware setting must be written to the corresponding registers of the processor. Because of the strict 32-bit architecture of the ARM cores, all registers are accessible on 32-bit addresses and are 32-bit wide. As already mentioned in HW_DEVELOPMENT, the GPIOs are bundled to five banks with up to 32 pins, which can be set with writing a logical '1' to the corresponding bit in the banks SET register and are deleted by writing a logical '1' to the corresponding bit in the banks CLR register. Writing a logical '0' to one of these registers has no effect. The procedure of using two different registers to set and delete a pin is not common but allows an interrupt-stable programming and write- or read-access to all to the corresponding register attached pins in only one clock cycle. On regular (non-GPIO) registers, setting and deletion of a bit is done in the same register. Beside the GPIO configuration, the processor contains a lot more set up registers for the several interfaces, which partially need many configuration data. The general access to the registers is firstly possible directly on the 32-bit address or secondly with pointer variables to these addresses. The first method is easier and faster usable because no additional file containing all the pointers must be written. On bigger projects, the second method is advisable because the code becomes much more read- and serviceable if the pointers are named like the corresponding registers in the processor user manual. Appropriate files containing already defined pointers are available for most ARM processors in example projects of development board manufacturers. In this thesis, this file is called LPC23xx.h and contains individual pointers to all accessible registers.
The application of pointers allows direct access to the registers but also requires detailed knowledge of bit-manipulation. It is always advisable to only change the actual bit(s) with logical AND or OR assignments. When using this, it is not possible to set and clear bits in a register within one step. This must be done successive. The only exception is to change the complete register value coevally, which should only be used if the non-actual bits do not matter or are not used. Otherwise, certain initialisation or function sequences could be disturbed by setting foreign bits in wrong moments. The following code fragment (code 2) shows the definition and usage of register pointers to set and delete a pin with an attached LED.
The next code fragment (code 3) shows a typical register set up with predefined bit-masks and afterwards logical assignments to set or clear certain bits in a register. As shown, the first writing to the register overwrites every available bit, because this special register is not used before this statement and all other important bits are changed afterwards. This style of code-writing is more extensive but on the other hand easier readable and serviceable, because the use of the mask names shows at first sight, what part of the configuration is affected and the used method of writing the operator shows directly if the corresponding bit(s) are set or deleted. To get to know the meaning of a set or cleaned bit in a register, the mask definitions are commented with their effects to the processor.
/* Fast Input/Output pin setup registers in LPC23xx.h */
#define FIO_BASE_ADDR	0x3FFFC000
#define FIO4DIR (*(volatile unsigned int *)(FIO_BASE_ADDR + 0x80))
#define FIO4PIN (*(volatile unsigned int *)(FIO_BASE_ADDR + 0x94))
#define FIO4SET (*(volatile unsigned int *)(FIO_BASE_ADDR + 0x98))
#define FIO4CLR (*(volatile unsigned int *)(FIO_BASE_ADDR + 0x9C))

/* LED Mask definitions in LED.c driver file */
#define LED0_MASK 0x00000010 /* LED is attached to pin 4 (Bit 4) of bank 4 (P4.4) */

    FIO4PIN |= LED0_MASK; /* Set pin 4 of bank 4 as output */
    FIO4SET = LED0_MASK; /* Switch on LED by setting corresponding pin */
    FIO4CLR = LED0_MASK; /* Switch off LED by deleting corresponding pin */
Code 2: Example of register manipulation to set and clear an external pin
If a mask is used in Eclipse, the mouseover-display shows its comment, although the definition is outside of the actual screen or even the file. This special behaviour is shown in figure 1, where the mouse (not visible) points to the EMC_WRITE_PROTECT mask.
/* static RAM access register configuration in LPC23xx.h */
#define EMC_BASE_ADDR 0xFFE08000
#define EMC_STA_CFG0 (*(volatile unsigned int *)(EMC_BASE_ADDR + 0x200))

/* EMC CONFIGURATION REGISTER MASKS in EMC.c */
#define EMC_BANDWIDTH_8 0x00000000 /* Bit 0-1. 00: 8 Bit */
#define EMC_PAGE_MODE 0x00000008 /* 1: Async mode, 0: disabled */
#define EMC_CS_POLARITY 0x00000040 /* 1: Active HIGH, 0: active LOW */
#define EMC_EXTENDED_WAIT 0x00000100 /* 1: EW enabled, 0: disabled */
#define EMC_BUFFER_CONTROL 0x00080000 /* 1: Buffer enabled, 0: disabled */
#define EMC_WRITE_PROTECT 0x00100000 /* 1: protected, 0: not protected */

/* Set up Static Memory Configuration Register in EMC.c */
    EMC_STA_CFG0 = EMC_BANDWIDTH_8; /* 8 Bit Buswidth and Register Reset */
    EMC_STA_CFG0 |= EMC_PAGE_MODE; /* Async Page Mode */
    EMC_STA_CFG0 &=~EMC_CS_POLARITY; /* Active LOW Chip Select */
    EMC_STA_CFG0 &=~EMC_EXTENDED_WAIT; /* Extended Wait disabled */
    EMC_STA_CFG0 &=~EMC_BUFFER_CONTROL; /* Write Buffer enable */
    EMC_STA_CFG0 &=~EMC_WRITE_PROTECT; /* No write protection */
Code 3: Example of the register manipulation codestyle with set and clean statements

Figure 1: Example of the mouseover-display function in Eclipse IDE
A last option to manipulate the processor registers is to build structures of every register with members for all mated bits. This method allows an easier usage, because the members can be used as normal variables and so set and clean bits within one logical step. The disadvantage of this method is the high effort to create the structures as well as the fact that the compiler will build the same bit manipulation commands like the method shown in code 3, with the difference that the structure method does not show exactly what the compiler will generate of the code.
Because the software development is for most parts done on other devices than the target tester board, the individual hardware-using software segments are switchable between three different hardware environments by changing only the switch. These environments are firstly a development board from the manufacturer Olimex, a company-intern product called IO-Controller, which is in several parts similar to the tester board, and lastly the tester board itself. Code 4 shows the switch definition and the general usage within this thesis. The keyword \MARK is a part of the Eclipse task function, which allows to mark codelines or -sections with several, self-created keywords like for instance \TODO, \NOTICE, \MARK. The slash identifies the following word as a task keyword. All lines marked this way are mentioned in the Eclipse task window and allow a direct step to this line or section. This allows a better abridgement.

/* Pinset Switch declaration and definition in LPC23xx.h */
/* For Olimex DemoBoard : PINSET_TESTER = 0
 * For Pinsettings of IO-CTRL REV_C: PINSET_TESTER = 1
 * For QUA_2475_TESTER : PINSET_TESTER = 2*/
#define PINSET_TESTER 2

/* PINSET_TESTER switch usage in example file (dac.h) */
// \MARK NEW PINSETTINGS FOR TESTER (2)
#if (PINSET_TESTER == 2)
#define maxDAC_Channels 6 /* If actual board is tester, set 6 DAC channels */
#else
#define maxDAC_Channels 4 /* If other board than tester, set 4 DAC channels */
#endif
Code 4: Definition and usage of the pinset switch
    1. FreeRTOS operating system
The FreeRTOS[2] is an open source operating system for embedded systems and is available for many different processors. It is free usable for private as well as commercial applications, but without any warranty. The operating system is already ported to the LPC23xx processor family, which allows an easy usability and require just minor customising to the tester application, such as memory allocation. FreeRTOS contains realtime behaviour, and beside of that multitasking functionality, time basics and semaphores.
[2] FreeRTOS:	Free realtime operating system
The multitasking principle is in fact just an illusion, because every conventional processor can only execute a single command per cycle. The trick is to rapidly switch between single tasks and make it appearing like multiple tasks are running concurrently. This is shown in figure 2, where the upper graph displays the subjective and the lower graph displays the real behaviour of the system. The order, in which the individual tasks are executed after another can be affected by the priority assigned to every new task.
FreeRTOS requires at least one task running in an endless loop. This is caused by the fact that the complete operating system consists of a simple application that is ended, if no more code is available to execute. As long as the so-called idle_task runs, the system remains active and new functions and tasks can be called or created (for instance by interrupts or remote calls). The idle_task of FreeRTOS is comparable with the idle task of other operating systems like Windows or Unix. New tasks are created with xTaskCreate with parameters like the function name, function arguments, the task priority and the stack size. The task management system is based on the principle of endless tasks, which means that tasks that ends because their code ends are not deleted. They can be started again without any need to recreate them. So of course they also block memory in the stack if they are just ended and not deleted with the command xTaskDelete.
Figure 2: Multitasking principle of FreeRTOS (source: FreeRTOS.org)
Time basics are of great importance in real time systems. The operating system is able to create a quite simple usable time stamp in milliseconds. This allows to directly handle with times within the code. The command vTaskDelay in combination with a time in milliseconds as parameter forces the system to hold the containing process or task for the given time. Thus, almost 100 per cent of calculation time becomes available for other processes.
Semaphores guarantee the exclusivity of functions. Even in stressed and critical situations, a real time operating system needs to keep its ability of forecasting. In many cases, more than one process are able to access a certain function or variable. In critical situations, these parallel-accessible functions must be secured of a simultaneous access. Usually, this is done by flags behaving like normal variables which are changed and asked for their value. Although this method is the more simple one, it contains a important disadvantage: the setting of a normal variable may take more than just on calculation cycle, and with this the exclusivity of a certain, secured software sequence is not warranted. The more technical form for this is devideable. In contrast to that, semaphores are undevidable. In FreeRTOS, semaphores are from an own type and are taken and released instead of set and cleaned like flags. Before semaphores may be used, they must be created. This is done with vSemaphoreCreateBinary. The function xTakeSemaphore returns a numeric value that indicates if the semaphore was taken or not. The software then is able to ask for this and act further. Exceptions are numeric semaphores; they are able to be taken multiple times up to a defined maximum. With xReleaseSemaphore, a semaphore is freed for a new access. If multiple processes try to access an already taken semaphore, FreeRTOS will not create some kind of queue list for it. The access will be given to the first process in stack. Also a queue list based on priorities is not possible, which turns the securing process based on semaphores to a serious task.

    1. Drivers
The drivers sub-project contain all functions necessary to access all internal or external attached periphery, which also includes special hardware configurations as mentioned in 1.1.2. Hardware configuration on page 2. Hereby each periphery or device got an own driver structure, which consists of a header- and a codefile (see figure 3). If a certain periphery becomes more complex (like for instance an USB stack), the code should be divided to more than two files and arranged to an own subfolder. The basic idea of this structure is a maximised dynamical usage.
Each driver contain an initialisation function, which sets hardware configurations (e.g. pin settings), starts up or loads special interfaces, allocates memory and sets the periphery to a certain start condition. In the following, functions to interact with the corresponding periphery are available within the codefile, for instance read and write functions on the memory drivers or special algorithms to build SPI commands and the like. Each of those functions, that should be available from outside of the corresponding codefile is declared in the drivers headerfile. Also, driver-specific type definitions, settings and variables, which should be used from other functions, are declared in the header. With this method is is possible to simply include the drivers headerfile to an application file and with that get full access to all data types, functions and drivers-specific variables.
Figure 3: Driver file structure
The initialisation functions are usually called from the main function right before the operating system becomes active. On the initialisation sequence, a certain order must be complied, because some peripheries depend on each other, as for instance the EEPROM depends on the SPI bus. In general, the whole driver subproject should contain as less dependencies and interactions with other projects as possible. In the actual software, the drivers only depend on the register-definition file LPC23xx.h, the custom data type definition file types.h and in some cases on parts of the operating system.
    1. Communication protocol
The communication protocol is used to transfer commands and data between at least two environment devices and is based on a Master-Slave principle. This means that the devices within the communication are not equal but depend on the master. The advantage of this bus architecture is an easy development, the drawback is the total dependency of the communication on the master device.
The used protocol is based on a company-intenal, general communication system and was specialised to the purpose of this thesis. All devices within the bus contain an own device number between 1 and 256, where 1 stands for the master and all numbers above for slave devices. Beside of this, every device must contain the highest used number and with this know the total number of devices within the bus. On several functions like the in- and output drivers it is possible to choose the device on which the command is to execute. This is realised by handling the device number within the function call. Although it is possible to execute a command on the own device by choosing the own device number,. Device number 0 always stands for the self device and does not make use of the protocol.
The interchange of commands and data happens in cycles stimulated by the master device. Each cycle belongs only to one slave device within the bus, where at first the master transfers his commands and data and afterwards receive results or function calls. The slave also transfers a cycle finished symbol, which enables the master to start the next cycle on the next slave device.
The bus architecture interferes with the operating system and initialises an own task on its start up. All functions called from the bus are executed within this special task to prevent collisions with the regular running software. Beside of the task creation, the bus initialisation also registers a device to a certain number and with this either to be the master or a slave. The registering is also bound to a certain communication interface, which is in this thesis on of the RS 485 front ends. On switching to a different interface, the cycle timings may be retuned. The communication protocol is multiple usable at the same time, which means that a device for instance may act as master for one bus and as a slave on a second bus. Because of that, the binding to an interface is marked in a bus handler variable with which it is possible to identify each bus affiliation.
The function management is based on two different bus function types, where one is a regular call and the other is a result call. The difference between them both is the moment on which they are called; the regular function is always executed in the beginning of a cycle and a result function at the cycle end. With this, it is possible to command a device to a certain task and to receive a result of this task within one cycle. This fact gets more important the more devices are involved to the communication structure. Functions must be shared to the bus in order to be able to execute them remotely. Each device contains two function pointer arrays in which the attached regular and result functions are listed. A function is attached with bpAttachRpc (for regulars) or bpAttachRpcResult (for results). The attaching requires parameters, which consist of a individual function number and the number of maximal parameters that should be transferred within the remote call to this function. If no parameters are necessary, the number of parameters fr attaching is NULL. A remote function call consist in fact of the transfer of the individual function number and an optional list of parameters.
Table 1 shows an example use of the bus protocol. The mentioned software activity is placed in only one bus communication cycle
Table 1: Communication protocol command and data flow example
Master	Slave
Bus initialisation
Initialise device as master / Attach a result function - Parameter: X / Functions checks the incoming result and prints out the parameter X. / Attach a regular function - Parameter: Y / Function checks the incoming parameter Y, prints it and, depending on it, sends a result. / If Y equals 1: print Y and send 5 as result / If Y is not 1: print Y and send 3 as result	Initialise device as slave
Software activity
Call regular function on slave – handle 5 as parameter / Print received parameter – Y = 5 / Send result to caller – Result = 3 / Result function is called / Print received result – Result = 3	Regular attached function is executed

    1. Test applications
The test applications are the main adapted part within this thesis and are split into two different sections and folders. Firstly, the tester contains several self-test applications to assure its functionality. The second kind of applications represents the remote hardware design test functions. Most of the self-test and remote test sequences are based on the same principles but are realised in different ways, which is mainly caused by the fact that the self-test has not to be as automated as possible and will rarely be executed.
In order to keep an overview, the test application files creation is based on the same principle already known from the drivers project; a header file for all prototypes, global defines and type definitions and a code file for the software. Every file that directly contains test applications is marked with the prefix “test” within its filename. The self-test folder solely consists of files like this. The remote test applications additionally require special driver software for the communication with the other bus device.
The individual test procedures are all based on the deliberations of chapter CONSIDERATIONS on page XYZ. In order of a dynamical use, each test consist of a general execute function which controls the further test procedure. If a certain test should be executed, only this function of type BOOLEAN is to be called. All further, individual test functions as well as the test result calculation for this periphery is done within the general execute function, which at its end returns the calculated test result.
The remote test functions partially are based on complex communication with included wait states realised with semaphores. For that reason, these test applications need an own initialisation sequence to create and take the semaphores. Because the operating system will collapse if a semaphore is taken or released without its previous creation, the semaphore-using functions must be secured against non-initialised access. This is most easily done with a BOOLEAN flag. Each individual semaphore-using test sequence got an own, global flag which is set to FALSE on start up and set to TRUE if the corresponding test initialisation is finished.
Each test is totally independent from the other tests. This is mainly caused to be able to call each sequence individually. In order to achieve a highly automated test environment it is necessary to create an fully automated test routine based on the single tests. Within this it is advisable to acquire and apply a logical order and to react on and interact with previous results. Table 2 shows the applied test sequence order and the possible dependences on other test parts.
Table 2: Test sequence order of the automated test application
Communication test	If fails complete test routine is unusable
LED test	No dependencies or restrictions
SDRAM test	Operating system may be booted with errors
EEPROM test	No dependencies or restrictions
Digital in- and outputs	No dependencies or restrictions
Analogue in- and outputs	Impossible if 4. failed
Relay throughputs	No dependencies or restrictions
Ethernet uplink	No dependencies or restrictions
Ethernet switch	Impossible if 8. failed
CF reader	No dependencies or restrictions
USB host	No dependencies or restrictions
CAN interface	No dependencies or restrictions
Analogue calibration	Impossible if 4. failed
Calibration check-up	Impossible if 4. or 13. failed
Optional tests on the extension board
EEPROM test	No dependencies or restrictions
Digital in- and outputs	No dependencies or restrictions
Analogue in- and outputs	Impossible if 15. failed
Relay throughputs	No dependencies or restrictions
Analogue calibration	Impossible if 15 failed
Calibration check-up	Impossible if 15. or 19. failed

    1. Additional software
Within the application project also some additional software parts are implemented to simplify the tester usage. Mainly this is the menu structure, which enables the user to interact with the test environment. The menu architecture is leaned to a common Linux terminal structure but is limited to more general abilities. The menu basically consists of four different arrays, of which the first contains the command, the second the corresponding function pointer, the third an calculation offset and the last some optional help text strings. The recognising of an command is built with string comparison. To reduce this intensive compare calculations, the command table is ordered alphabetically. Before the complete command is processed, the first character of the command is compared with the offset table. If commands with this first character are available, the offset of this character for the command table is returned and enables the menu to start comparing the commands at the first entry with the given character. The offset table is built and calculated within an menu initialisation function, which must be called before using the menu.
The menu terminal is able to handle a maximum of three 32-bit arguments, which can be handled directly next to the command. The differentiation between command and arguments is done by the standard function strtok, which is able to divide a string to several so-called tokens. This division is based on a character list, which must be handled to strtok as well. Every time strtok detects on of the characters given in the list, a new token will be split. The divider characters are not handles to any token.
At least, it is possible to print out short help messages for each available command. This is done with attaching the suffix “_help” to a command. The printed aid shows the use of the corresponding command and optional or required arguments.
  1. Test item

    1. Test software integration to the existing software
Unlike the tester board the test item operating system is based on an actual Linux Kernel version implemented to a small and limited Linux environment. Because of that, the integration of specific test software is more complicated and requires an development environment which is especially build for the applied processor. This is done with the Buildroot package, which is able to be set to several different processors and periphery and with that compile the software written for the test item.
    1. Communication
The communication protocol source code in the test item is in most parts similar to the code used on the tester hardware. In contrast to FreeRTOS it is not easily possible to embed the protocol to the Linux operating system. This is because the kernel and the surrounded operating system are already compiled and built to the test item. A second difference is the interface used to communicate, which is unlike to the tester on the test item managed and controlled by Linux as well.
To solve these problems it is necessary to reconfigure all functions that directly handles variables and data flow between the protocol and the operating system. These are the write and read functions on the interface and the protocol-internal task management. ANSI C enables interaction between binary code files and the operating system, which allows an uncomplicated cooperation.
    1. Script and C-Code development for individual test applications