Test application run cycle
Due to the mentioned circumstances, it was only possible to finish one of the required test applications in time. The remote digital (MB) connectivity test is so used as example.
Figure 1 shows the called test output and result received in a terminal window. Each line test consists of three different result. The first stands for the LOW read-back test, the second for a check if all other channels remain LOW if the tested one is set to HIGH and the last one represents the HIGH test. If only one of these tests fail, the over-all test result is set to false.
Figure 2 lists the log output of the digital test shown in figure 1. Apart from the pure messages, the different message urgencies and the message directions are written to the log. The urgency of a message may be used to ignore or highlight certain messages like results or warnings.
Figure 1: Terminal output of the remote digital (MB) connectivity test
The screenshot shown in figure 3 displays the control application with the applied test. As seen, the message output equals with picture 1. It is obvious that the keyword detection routine had found the right test result and made this result visible by colouration of the digital (MB) test status textbox. Because no other test is available within the control application, the statistic section already shows a passed test.
Serial Port: COM2 Direction: Input Urgency: menu Message	dio 2
Serial Port: COM2 Direction: Output Urgency: test Message	Linetest for Digital Output (MB) 0:
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	Linetest for Digital Output (MB) 1:
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
[...]
Serial Port: COM2 Direction: Output Urgency: test Message	Linetest for Digital Input (MB) 0:
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	Linetest for Digital Input (MB) 1:
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
Serial Port: COM2 Direction: Output Urgency: test Message	PASSED
[...]
Serial Port: COM2 Direction: Output Urgency: result Message	DIO Test	PASSED
Figure 2: Log output of the remote digital (MB) connectivity test

Figure 3: C# control application with passed remote digital (MB) test