Merging of tester and test item
The following sub-chapters will deal with the problems occurred during the consolidation. From the beginning of this thesis it was expected that this part of development will cause problems which need to be fine-tuned and/or solved. Due to the circumstance of the used alternative hardware (see chapter XYZ INTRODUCTION on page ZYX), several more problems and workarounds occur during the consolidation. As far as possible it must be taken into account that the workarounds are functional on the alternative devices.
  1. Analysis and solution of accrued problems
    1. Communication
The communication between both devices is based on an already finished and proved communication protocol. It stands for one of the major parts of the development, because the complete environment is based on this.
Originally it was expected that the implementation of this protocol will only cause minor problems concerning the task stack size and minimal timing difficulties. During the consolidation it turned out that the communication protocol is based on a half-duplex communication interface. This means that a member of the communication can either read or write but is not able to do both coevally. In general, a RS 485 interface is built in full-duplex with five wires, of which two represent plus and minus either for transmit and receive and the fifth line represents the interface GND signal. The mode-reducing is effected by an special component. It is built to normally just read from the interface and only to be enabled to write by setting the ENABLE signal. The special component with its internal connection is shown in figure 1.
In the considerations it was expected that the test item also contains two half-duplex RS 485 interfaces. During the first communication attempt this mistake was found because the protocol was not able to establish a connection. During the debugging phase it turned out that the testee was either able to send or to read. But the normal protocol functionality includes confirmation as well as pure data packages which comes out to the fact that a normal operation is only possible with a two-way communication. Even without confirmation data transfer in both directions is necessary because the test item needs to send test results back to the test device.
Figure 1: RS 485 full-to-half-duplex mode changer
There are five possible solution statements for the communication problems, which more or less interfere with the hard- and/or software of both devices. Firstly it is possible to change the testers RS 485 interface to full-duplex mode as well. On first sight this seems to be the easiest solution. Beside of the complex patchwork on the test device PCB this possibility also enforces changes to the interface driver software as well. Another reason against this option is the fact that the PCB changes are not allowed to be done on the alternative hardware. Because of that, no further development would be possible as long as the tester device becomes available, which costs a lot of time. Thus this possibility is no option. The second possible solution would be the modification of the full-duplex interface on the test item. In fact this option requires at first the patching and afterwards the de-patching of the RS 485 connection and also changes to the Linux kernel system, which makes this solution even more unhandy than the first one. A third solution is an additional piece of hardware which is connected to the RS 485 interface of the test item and reduces the transfer to half-duplex mode. Although this option does not require any patchwork it costs develop- as well as assemble time and enforces changes to the Linux kernel as well as the second option. As a forth option it is possible to change the communication interface. Basically a RS 485 interface is driven by an UART which means that any other UART connection may be used instead of the RS 485 connection. The test item contains one more interface driven by an UART, which is the RS 232 serial connection. Unfortunately this connection is already used by the operating system as standard input and output for commands and messages. With the use of this connection for the communication it will not be possible any more to interact manually with the Linux operating system. Also it would not be possible to print out messages to a terminal.
Lastly is possible to modify the protocol software on the test device to use both available RS 485 interfaces to create a full-duplex transfer. The advantage of this method is that no patchwork is required and that this solution is runnable both on the original test device as well as on its alternatives. Furthermore the required software changes are minimal because in the end only the central read and write calls must be modified to work with the right interface. Fortunately this both calls are each only once used in the protocol and are not able to collide. In order to be able to modify the interface number used to write and read, the protocol initialisation is extended with arguments to set these configuration manually.
    1. test sequences

  1. Adjustment of applications
Several parts of the software require a fine-adjustment or special additions in order to create a fully applicable test environment. This mostly concerns the communication between both devices as well as necessary wait-states on certain code locations.
    1. Remote access
The communication protocol is a circular system. This means that a call from outside is usually not executed immediately but on the next cycle. This certainty causes a natural delay

waitstates bei settings
  1. Development and Adjustment of result calculating applications