Considerations
The considerations are the first step in development of test environments. In general, they consist of a list of components, interfaces, connections and software parts that should be proved on the test item and corresponding to that a list of possible methods to apply these tests. The test item was introduced in chapter TESTE on page XYZ. From this and other influences like already existing resources and some other more, one or several options to design a specific test hardware are created. Within these considerations, not only technical but also economical issues should be mentioned. Lastly, the usability of the hardware must be considered, for instance the possible usage of operating systems or development and debugging software. With these information, the hardware assortment and with that the hardware design can be done.
  1. Tester hardware
the tester hardware is, as mentioned above, chosen by considerations with many different influences. As main processor and base of the test hardware, an 32-bit ARM7 microcontroller of type LPC 2388, manufactured by NXP, is chosen. This is mainly based on already existing resources and experiences within the company that supports this thesis, but also the controller specifications of 64 kB RAM, more than 80 GPIOs and the applied interfaces are advantages of this processor.
To test the several different in- and outputs of the test item, the same number and kind of inverted connections are attached to the tester. Especially the analogue connections but also the digital and relay in-,out- and throughputs must be able to drive the full range of the test item. The same number assures to be able to test every outgoing or incoming line of the testee individually. Although the processor includes several internal 10-bit ADCs and DACs, external devices with a higher resolution and more channels will be used. The high resolution is mainly necessary for the analogue connections calibration of the test item. Because the analogue lines of the test item are only to drive current, the converter circuits must be extended to this mode. Because the testee is expandable with an additional connector board with several more analogue and digital in- and output channels, the converters and the digital connections circuits are extended with multiplexers to switch between the common channels and the extension board.
For communication, the test board contains two RS 485 devices, a CAN and an ethernet interface, which all will be connected to the corresponding interfaces on the test item.

  1. Test scheme
  2. Test procedures
Table 1 shows all to be tested interfaces, connections, components and software parts with their corresponding test method, controlled by the specific test hardware.
Table 1: Comparison of test items and their corresponding test methods
	Item to be tested	Test method
Processor board
	Compact Flash reader
	Ethernet switch	Ping to an known server
	Ethernet uplink
	SRAM
	USB host controller
Main board
	Analogue input
	Analogue output	read single channel low value / read single channel high value / check if all other channels remain low
	CAN interface
	Digital input
	Digital output	read single channel low value / read single channel high value / check if all other channels remain low
	EEPROM
	Relay
	RS 485 interface
Extension board
	Analogue inputs
	Analogue outputs	read single channel low value / read single channel high value / check if all other channels remain low
	Digital inputs
	Digital outputs	read single channel low value / read single channel high value / check if all other channels remain low
	Relay