Testee
The testee is the device that should be tested. As mentioned in the task, it is created and designed to be used as a ship stabilisation system. The principle of this stabilisation is rather new and not well known to a broad public. It insists in fact of a artificial horizon device, weather and atmospheric sensors shared all over the ship and several fins and heavy weights build to the ship hull. With this the controlling device is able to compensate wave and wind influences and balance the ship to a cross-movement of just 0,7° to each side where it was before more than 10° per side. This balancing is done by moving the weights near to or away from the hull. Also, the system is able to compensate movements ahead or sidewards by moving and rolling the attached fins. The weights as well as the fins weigh several tonnes per part, so they are moved by strong engines, which are controlled but not directly powered by the testee device.
The main purpose of the system is the stabilisation of luxurious offshore yachts. Because of the high water-resistance of the weights, they can only be used when the ship stands still or moves very slow. The fins are designed to be used also while sailing and reduce the rolling of the hull on heavy sea. The main reason to implement a system like this to an offshore yacht was the problem to safely land a helicopter on a strong and incalculable moving and rolling ship. Also, yachts from that size often are too big to directly enter a port, which forces the owner to anchor outside in the unguarded sea. In this situation, the stabilisation system increases the comfort on the ship extensively. The figures 1 and 2 show the attached weights (figure 1) and fins (figure 2) in action. The figures are from demonstration and public relation video animations created by the customer company.

Figure 1: Yacht hull with attached stabilisation weights (video animation)
Figure 2: Yacht hull with attached stabilisation fins (video animation)
Apart from the main purpose of the device, there are several more functions it should fit to. Because luxurious yachts are equipped with a ship-internal network and attached to that a high-level multimedia system, the stabilisation system board can be integrated to this network up to a certain level, where the stabilisation of the ship is in every situation highest prioritised.
The complete controlling software is developed by the customer. The device is produced and afterwards delivered with a basic linux operating system that supports all available periphery. The test application environment developed with this thesis is placed in the production chain between the production and the delivery of the devices. Because the controlling software is not available, the purpose of the device is of minor importance to the further hardware design test.
The stabilisation system device insists of three different boards. This is mainly caused by the requirements of the customer for a better adjustment of the product to the future purpose; there is no technical need of division. Figure 3 shows the complete device with all three parts.

Figure 3: Overview to the complete testee device with all extensions
  1. Processor board
The processor board is the only “intelligent” part of the device. It contains every component directly required by the processor. This includes memory devices as well as interfaces.
As main processor, a Freescale MPC 5200 based on the PowerPC[1] architecture is used. Freescale (formerly Motorola) is, beside of Apple and IBM, one of the developers of this architecture and is nowadays one of the leading manufacturer for PowerPC chips. PowerPCs are often used in embedded systems because of their high performance and the ability to calculate with floating points in double correctness, which is interesting for measurement devices like the actual system. The PowerPC processors nowadays available are normally based on 64-bit architectures, only IBM supports some 32-bit chips. Beside of the embedded purpose, PowerPCs are used in almost all actual gaming consoles (Nintendo Wii, Microsoft Xbox, Playstation 3), in all Apple computers produced before the year 2006 and in high performance server stations and supercomputer grids (mostly from IBM). Also, the military industry uses PowerPCs, for instance in the latest U.S. pursuit plane F22 Raptor.
[1] PowerPC:	Performance optimization with enhanced RISC performance chip
Beside of the main processor, a co processor is used to control the inputs and outputs of the device. Although this causes a discharge on the PowerPC, the main reason for the second processor is the realtime behaviour. The linux operating system on the main processor is a non-realtime system, which means that the software can not warrant the exact time of input values. In contrast to that, the co processor only contains an cyclic, interrupt-based software that warrants the compliance of requested timings. The communication between both processors is mainly implemented with SPI, where the main processor represents the master device. Where all inputs are read circular, also the outputs are driven in the same cycles. The applied co processor is a NXP LPC 2108, based on the ARM[2] chip architecture. These chips became famous in the embedded and mobile sector within the last years because of their power saving features and the consequent 32-bit design. According to estimates, more than 75% of the used embedded 32-bit RISC processors are based on an ARM core. Famous example devices based on ARM processors are the iPhone and the iPod (both developed and traded by Apple) and the mobile gaming console DS (developed by Nintendo).
[2] ARM:	Advanced RISC Machine
Beside of the two processors, the most important components are the memory devices. The board possesses 128 MB SRAM and 64 MB FLASH, where the FLASH is used store the original software code, which is copied to and afterwards executed from the SRAM on a boot up. Furthermore, the processor board insists of a eight-port ethernet switch, a ethernet uplink port, an USB host interface connector and a CF[3] card reader. Lastly, the processor board content several connector interfaces for different purposes; for instance a JTAG connection for debugging, RS 232 connections to program and communicate with both processors and three connector rows at the bottom side of the board to establish connections to the peripheral devices on the other boards.
[3] CF:	Compact Flash
  1. Main board
The main board is the biggest part of the stabilisation system device and is used to mount on the one hand the system to a rack and on the other hand the processor and the extension board to itself. Furthermore, it contents the basic input and output connections available on the system and provides the complete power supply of the board, inclusive the step-down stages and fuses.
The connector periphery consists for most parts of the analogue and digital inputs and outputs, of which each eight channels are available. Only the analogue inputs contain six channels. The digital connections work with industrial standard logic of 24 V, the analogue connections are only used to drive and read current between 0 and 20 mA. In addition, four relay throughputs are implemented to the main board, which allow to switch an incoming signal directly to an outgoing. Lastly, a CAN and two RS 485 ports complete the connection section. Because the additional extension board can be mounted to the main board as well as the processor board, there is one more signal connector available to attach the extension board to the system.
The main board contains an 64 kB EEPROM, which is to store the analogue calibration values. This is mainly caused by the consideration to be able to use the board in different vicinities with different processor boards without the need to recalibrate the processor to the new analogue connections.
  1. Extension board
The extension board is an additional component of the stabilisation system to extend it with more analogue and digital connections and relay throughputs. In fact, the extension board contains eight more analogue inputs, six more analogue outputs and both four more digital in- and outputs. Furthermore, two more relay throughputs are available with this extension.
All in-, out- and throughputs are attached directly connected to the co processor on the processor board through a connector placed on the main board. The power supply is done by a special power connector from the main board.
As well as the main board, the extension board contains an own 64 kB EEPROM to store the calibration values for the analogue connections.