Considerations
The considerations are the first step in development of test environments. In general, they consist of a list of components, interfaces, connections and software parts that should be proved on the test item and corresponding to that a list of possible methods to apply these tests. The test item was introduced in chapter TESTE on page XYZ. From this and other influences like already existing resources and some other more, one or several options to design a specific test hardware are to create. Within these considerations, not only technical but also economical issues should be mentioned. Lastly, the usability of the hardware must be considered, for instance the possible usage of operating systems or development and debugging software. With these information, the hardware assortment and with that the hardware design can be done.
  1. Test scheme
The test scheme shows the individual parts of the testee that should be proved and in addition to that possible test methods for each part. Furthermore, a general, logical test order sequence must be acquired.
The testing of the several single-channel connections is one of the biggest part of the whole test procedure. This section is split into the three different kinds of connections, which are digital, analogue and relay channels. For all of these, the test procedure is nearly similar; each channel must be proved to be able to drive the full signal range and not to be shorted to other channels. On the digital and relay channels, the full range consists of the two easy distinguishable BOOLEAN stats LOW and HIGH (digital channels) respectively OFF and ON (relay channels). The range of the analogue channels is prescribed by the converter-circuit, but beside the simple functionality, also offset and deviation of the converter and converter-circuit must be considered. Non-calibrated converters should be tested with wide tolerances. In order to test these single-channel connections, every kind of connection will get an opposite on the tester hardware in the same quantity. Because the testee is expandable to more in- and outputs and the test environment should remain highly automated, the tester must contain also additional connections. This could either be done with adding more analogue, digital and relay circuits to the tester board or with multiplexing the already existing channels between different connectors. In order so reduce costs both of components as well as on the size of the board, the multiplexing method is advisable, also because the channels will not be used all at the same time.
To test the USB and CF host controller and interfaces, it is sufficient to attach an appropriate memory device and mount it in the Linux operating systems. This is caused by the fact, that the design test should only assure that all connections between an interface and its controller are routed correctly. So, a special, so-called “golden file” can be copied to the memory and afterwards be read back and compared with the original. If the comparison failed, it is hardly possible to suggest a possible reason, because both interfaces are more complex constructions. The easiest workaround is to check all connections manually.
The two EEPROM components located at the main as well as on the extension board are connected to the processor with the I²C bus interface. Several, individual test options are possible. In general, a memory attachment is tested by a systematic check of all address and data lines. Because of the special I²C link-up, this check is not required. To test the connection and functionality of the memory, it is sufficient to write and afterwards read back a test string. Depending on the size, the connection speed and the future purpose of the EEPROM, it is advisable to systematically write to and read from the complete memory to find defect bits. If it is known that just certain area of the memory will be used it is sufficient to just scan this sector for broken bits. Because of the size of 64 kB, a complete memory test will be applied. If both memory devices are not functional, it is obvious that the I²C interface is broken.
The CAN interface is easily testable either with an self-test mode or with an so-called “Hello world” test. The self-test does not require a second device that sends or listens to the bus but only assures that the devices transmit and receive connections work properly. One of the advantages of the CAN interface is to register it to certain addresses, that are sent with every message. With this, it is possible to group certain devices. With the “Hello world” test, the testee CAN is registered to an user-defined address and programmed to directly send back the incoming message. Afterwards, another CAN device sends an test string to this address. If the received string is the same than the send one, the interface works. The test name is based on the fact that test strings in the information technology are commonly and traditionally “Hello world”.
The RS 485 interfaces can be tested with two different methods. On the one hand it is possible to connect them both to each other and send test strings from one to the other. This method is most economic but, in case of an error, does not allow any suggest, which interface is broken. The second option is to attach two RS 485 interfaces also to the tester board and connect them to the test items. Because of the low costs of RS 485 transceivers the higher comfort of two own RS 485 interfaces outweighs the economic advantages.
The remaining connections like the JTAG or the RS 232 interface can be tested on several different methods. The JTAG and one of the eight ethernet switch ports are necessary to copy the software to the board. The only method to test their functionality before any code is copied is to measure the wires manually. The programming of the board is most complex part for debugging because it is hardly possible to suggest any reason for a certain functionality disorder. In general it emanates from that the connections are fine if the copying is successful. Nevertheless it is possible but not necessary to implement a special test routine for the JTAG interface. The RS 232 of the main processor is used as standard input and standard output of the Linux terminal. Although more complex tests with different transfer speeds can be created, it is sufficient to test if the terminal of the board is accessible with the standard serial port settings already implemented in the Linux operating system, which are set to the maximum transfer rate.
The ethernet interface can be tested on two different ways, which depend on the surrounding. If available, the testee should be connected to an already installed network with its uplink port. With this it is possible, to execute an ping command to an known server, which, if available, answers with an pong. The readback of this action can be evaluated. Although the functionality of the switch components is already assured by the software copying, it is advisable to test all available ethernet ports. For that, the switch can also be connected to the network, but it is important to only connect one port simultaneously, because it is otherwise not possible to get to know on which port the device pinged. A more advisable method is an ethernet connection from the tester to the testee switch. Because of the uplink port connection to the network, the tester is so able to reach the network through the switch. In order to automate this, it is possible to insert an 8-way multiplexer into this connection to test all eight switch ports on after another. Although this method is rather comfortable, it causes high costs, because of the high signal frequencies of the ethernet connection that must be multiplexed. To reduce the costs, the single line connection method is chosen and in addition, the software will force the user to switch the cable between the eight ports manually.
Kalibrierung
  1. Tester hardware
the tester hardware is chosen by considerations with many different influences. As main processor and base of the test hardware, an 32-bit ARM7 microcontroller of type LPC 2388, manufactured by NXP, is chosen. This is mainly based on already existing resources and experiences within the company that supports this thesis, but also the controller specifications of 64 kB RAM, more than 80 GPIOs and the applied interfaces are advantages of this processor.

  1. Test procedures
Table 1 shows all to be tested interfaces, connections, components and software parts with their corresponding test method, controlled by the specific test hardware.
Table 1: Comparison of test items and their corresponding test methods
	Item to be tested	Test method
Processor board
	Compact Flash reader	Mount an attached memory device / Test write and read on memory
	Ethernet switch	Ping to an known server through the uplink port for each port individually
	Ethernet uplink	Ping to an known server
	SRAM
	USB host controller	Mount an attached memory device / Test write and read on memory
Main board
	Analogue input	Stimuli read by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	Analogue output	Stimuli written by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	CAN interface	Receive and return a test string from and to tester board
	Digital input	Stimuli written by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	Digital output	Stimuli read by tester board / Write single channel low value / Write single channel high value / Check if all other channels remain low
	EEPROM	Test write and read on all memory section
	Relay	Switch incoming voltage; readback on tester
	RS 485 interface	Receive and return a test string from and to test board
Extension board
	Analogue inputs	Stimuli read by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	Analogue outputs	Stimuli written by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	Digital inputs	Stimuli written by tester board / Read single channel low value / Read single channel high value / Check if all other channels remain low
	Digital outputs	Stimuli read by tester board / Write single channel low value / Write single channel high value / Check if all other channels remain low
	Relay	Receive and return a test string from and to tester board