Test item
The testee is the device that should be tested. As mentioned in the task, it is created and designed to be used as a ship stabilisation system. The principle of this stabilisation is rather new and not well known to the general public. It in fact consists an artificial horizon device, weather and atmospheric sensors shared all over the ship and several fins and heavy weights built to the ship hull. With this the controlling device is able to compensate wave as well as wind influences and to balance the ship to a cross-movement of just 0,7° to each side. Before this was more than 10°. This balancing is done by moving the weights near to or away from the hull. Moreover, the system is able to compensate movements ahead or sidewards by moving and rolling the attached fins. The weights as well as the fins weigh several tonnes per part, so they are moved by strong engines, which are controlled but not directly powered by the testee device.
The main purpose of the system is the stabilisation of luxurious offshore yachts. Because of the high-water resistance of the weights, they can only be used when the ship stands still or moves very slow. The fins are designed to be used also while sailing and to reduce the rolling of the hull on heavy sea. The main reason to implement a system like this to an offshore yacht was to solve the problem of safely landing a helicopter on a strong and incalculable moving and rolling ship. Also, yachts from that size often are too big to directly enter a port, which forces the owner to anchor outside in the unguarded sea. In this situation the stabilisation system increases the comfort on the ship extensively. The figures 1 and 2 show the attached weights (figure 1) and fins (figure 2) in action. The pictures are from demonstration and public relation video animations created by the customer company.

Figure 1: Yacht hull with attached stabilisation weights
Figure 2: Yacht hull with attached stabilisation fins
Apart from the main purpose of the device, there are several more functions it fulfils. Because luxurious yachts are equipped with a ship-internal network and attached to that a high-level multimedia system, the stabilisation system board can be integrated to this network up to a certain level, where the stabilisation of the ship is in every situation highest prioritised.
The complete controlling software is developed by the customer. The device is produced and afterwards delivered with a basic linux operating system that supports all available periphery. The test application environment developed within this thesis is placed in the production chain between the production and the delivery of the devices. Because the controlling software is not available, the purpose of the device is of minor importance for the further hardware design test.
The stabilisation system device consists of three different boards. This is mainly caused by the requirements of the customer for a better adjustment of the product to the future purpose; there is no technical need for division. Figure 3 shows the complete device with all three parts.

Figure 3: Overview to the complete testee device with all extensions
  1. Processor board
The processor board is the only “intelligent” part of the device. It contains every component directly required by the processor. This includes memory devices as well as interfaces.
As main processor, a Freescale MPC 5200 based on the PowerPC[1] architecture is used. Freescale (formerly Motorola) is, along with of Apple and IBM, one of the developers of this architecture and is nowadays one of the leading manufacturers for PowerPC chips. These are often used in embedded systems because of their high performance and the ability to calculate with floating points in double correctness. This is interesting for measurement devices like the actual system. The PowerPC processors nowadays available are normally based on 64-bit architecture, only IBM supports some 32-bit chips. In addition to the embedded purpose, PowerPCs are used in almost all actual gaming consoles (Nintendo Wii, Microsoft Xbox), in all Apple computers produced before the year 2006 and in high performance server stations and supercomputer grids (mostly from IBM).
[1] PowerPC:	Performance optimization with enhanced RISC performance chip
Additionally to of the main processor, a co-processor is used to control the inputs and outputs of the device. Although this causes a discharge on the PowerPC, the main reason for the second processor is the real-time behaviour. The linux operating system on the main processor is a non-realtime system, which means that the software can not warrant the exact time of input values. In contrast to that, the co-processor only contains an cyclic, interrupt-based software that warrants the compliance of requested timings. The communication between the processors is mainly implemented with SPI[2], where the main processor represents the master device. Inputs as well as outputs are driven in the same cycle. The applied co-processor is a NXP LPC 2108, based on the ARM chip architecture. These chips became famous in the embedded and mobile sector within the last years because of their power saving features and the consequent 32-bit design. According to general estimates, more than 75% of the used embedded 32-bit RISC processors are based on an ARM core. Famous example devices based on ARM processors are the iPhone and the iPod (both developed and traded by Apple) and the mobile gaming console DS (developed by Nintendo).
[2] SPI:	Serial peripheral interface
Except for the two processors, the most important components are the memory devices. The board possesses 128 MB SRAM[3] and 64 MB FLASH, where the FLASH is used to store the original software code, which is copied to and afterwards executed from the SRAM on a boot-up. Furthermore, the processor board consists of a eight-port ethernet switch, a ethernet uplink port, an USB host interface connector and a CF[4] card reader. Finally, the processor board contains several connector interfaces for different purposes; for instance a JTAG connection for debugging, RS 232[5] connections to programme and communicate with the processors and three connector rows at the bottom side of the board to establish connections to the peripheral devices on the other boards.
[3] SRAM:	Static random access memory
[4] CF:	Compact Flash
[5] RS 232:	Recommended standard 232
  1. Main board
The main board is the biggest part of the stabilisation system device and is used to mount the system to a rack and the processor as well as the extension board to itself. Furthermore, it contains the basic input and output connections available on the system and provides the complete power supply of the board including the step-down stages and fuses.
Most parts of the connector periphery consists of the analogue and digital inputs and outputs, out of which each eight channels are available. Only the analogue inputs contain six channels. The digital connections work with industrial standard logic of 24 V, the analogue connections are only used to drive and read current between 0 and 20 mA. In addition to that, four relay throughputs are implemented to the main board, which allow to switch an incoming signal directly to an outgoing one. Finally a CAN[6] and two RS 485 ports complete the connection section. Because the additional extension board can be mounted to the main board as well as the processor board, there is one more signal connector available to attach the extension board to the system.
[6] CAN:	Controller area network
The main board contains an 64 kB EEPROM[7], which is to store the analogue calibration values. This is mainly caused by the consideration of being able to use the board in different vicinities with different processor boards without the need to recalibrate the processor to the new analogue connections. Figure X provides an overview of the whole connectivity. As shown, apart from the CAN and the RS 485, the different kinds of connections are not grouped to own connectors but are adjusted to the future purpose. This assembly is arranged by the customer. Also shown is the EEPROM in the upper left corner.
[7] EEPROM:	Electrically erasable programmable read-only memory (also E²PROM or E2PROM)

Figure 4: Overview of the mainboard connectivity
  1. Extension board
The extension board is an additional component of the stabilisation system to extend it with more analogue and digital connections and relay throughputs. In fact, the extension board contains eight more analogue inputs, six more analogue outputs and both, four more digital in- and outputs. Furthermore, two more relay throughputs are available with this extension.
All in-, out- and throughputs are attached directly connected to the co-processor on the processor board through a connector placed on the main board. The power supply is done by a special power connector from the main board.
As well as the main board, the extension board contains an own 64 kB EEPROM to store the calibration values of the analogue connections.